C.R. Laurence Co., Inc.		Distributed by ZeroDocs.com

This section includes editing notes to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by the following method in Microsoft Word:

Display the FILE tab on the ribbon, click OPTIONS, then DISPLAY. Select of deselect HIDDEN TEXT.

This guide specification section has been prepared by C.R. Laurence Co., Inc. for use in the preparation of a project specification section covering the Palisades S90 Bifolding Door and Wall System.

The following should be noted in using this specification:

Hypertext links to manufacturer websites are included after manufacturer names to assist in product selection and further research. Hypertext links are contained in blue, e.g.:

www.crlaurence.com

Optional text requiring a selection by the user is enclosed within brackets and as red text, e.g.: Color: [Red.] [Black.]"

Items requiring user input are enclosed within brackets and as red text, e.g.: "Section [__ __ __ - ________]."

Optional paragraphs are separated by an "OR" statement included as red text, e.g.:

**** OR ****

For assistance in the use of products in this section, contact C.R. Laurence Co., Inc. by calling 800-421-6144 or visit their website at www.crlaurence.com.

This specification has been prepared based on SimpleSpecs™ specification templates. The SimpleSpecs™ Master Guide Specification system comprises a full architectural master specification that can be used to specify all project requirements. For additional information on S-Specs products visit the ZeroDocs.com website at www.zerodocs.com.

SECTION 08 35 13 - ALUMINUM-FRAMED FOLDING DOORS

GENERAL

SUBMITTALS

Action Submittals:

Shop Drawings: Illustrate products, installation, and relationship to adjacent construction.

Product Data: Manufacturer’s descriptive data and product attributes for entrances.

Samples: [Selection samples.] [Verification samples.]

Informational Submittals:

Certificate of Compliance: Certification that installed products meet specified design and performance requirements.

SYSTEM DESCRIPTION

Aluminum Bifold/Pivot Doors:

AAMA/WDMA/CSA - 101/I.S.2/A440, Performance Grade CW40.

Thermal transmittance of door assembly: Maximum U-value of 0.36 BTU/square foot per hour per degree F, tested to NFRC 100.

Air infiltration: Maximum 0.05 CFM per square foot, tested to ASTM E283 and NFRC 400 at 6.24 PSF.

Water penetration: No uncontrolled water leakage, tested to ASTM E547 and E331 at 10 PSF.

Structural performance: Pass L/175 deflection at 50 PSF positive and 40 PSF negative, tested to ASTM E330.

Life cycle performance: Tested to 250,000 cycles.

Sound transmission class (STC): 33 to 36, tested to ASTM E1425.

Forced entrance resistance: Conform to AAMA 1304.

QUALITY ASSURANCE

Retain the following to specify minimum installer qualifications.

Installer Qualifications: Firm specializing in work of this Section with minimum [2] [__] years’ experience.

Retain the following for a full-size mockup.

Mockup: [One full sized system unit.] [____.] Approved mockup [may] [may not] remain as part of the Work.

PRODUCTS

MANUFACTURERS

Contract Documents are based on Palisades S90 by C.R. Laurence Co., Inc. www.crlaurence.com

- Edit the following to indicate whether substitutions will be allowed for the products in this section.

Substitutions: [Refer to Division 01.] [Not permitted.]

MATERIALS

Aluminum Extrusions: ASTM B221.

Glass:

Description: ASTM E2190, 1 inch thick sealed insulating.

Glass type: ASTM C1048, Kind FT fully tempered.

Interior lite: Clear.

Exterior lite: [Clear.] [[Bronze] [Gray] [Blue] [Green] [____] tinted.]

- Retain the following for low-e coated glass.

Low-e-coating: Located on [No. 2] [No. 3] surface.

Hardware: Stainless steel.

Concealed hinges.

Multipoint locking mechanism.

Rollers and track.

FABRICATION

Door Operation: Bifolding, bottom rolling, [outward] [inward] folding.

Size and Configuration: [____.] [Refer to Drawings.]

Frame and Panel Profiles:

Aluminum extrusions, center glazed, thermally broken.

System depth: 3-1/2 inches.

Sightlines: 4-3/4 inches.

Rails: 1-7/16 inches.

Sills: [Flush.] [Raised.]

Compensating channels and adjustable spacers.

Adjustable roller height. Plus or minus 1/16 inch.

Factory assemble doors into single units.

Weatherstrip operable sash and frame.

FINISHES

Retain the following for an anodized finish.

Aluminum: AAMA 611, Architectural Class I anodized, [clear.] [dark bronze.]

**** OR ****

Retain the following for an intermediate powder coating system with good weatherability and color retention.

Aluminum: AAMA 2604, [____] [custom] color [to be selected from manufacturer's full color range].

EXECUTION

INSTALLATION

Install in accordance with manufacturer's instructions and approved Shop Drawings.

Install glass as specified in Section 08 80 00.

Installation Tolerances:

Maximum variation from plumb or level: [1/32] [__] inch in 3 feet or [1/16] [__] inch in any 10 feet, whichever is less.

Maximum misalignment of members abutting end to end: [1/32] [__] inch.

Sealant space between system and adjacent construction: [3/8] [__] inch plus or minus [1/8] [__] inch.

END OF SECTION